## Slide 1: Adjoint Charge Deposition and CAD Transport in ITS
B. Franke, R. Kensek, H. Schriner, L. Lorence, and F. Gelbard
Sandia National Laboratories, 2001

## Slide 2: Charge Deposition
Net charge deposited is the difference between the removal and absorption of charged particles in a medium
Charge removal
  Interactions imparting energy to secondary charged particles
  The production of secondary charged particles above the cutoff energy due to Boltzmann interactions
Charge deposited
  Due to the “absorption” of charged particles slowing down in the medium
  Interactions that leave the particle with less than the cutoff energy due to either the CSD operator or an inelastic Boltzmann interaction
Adjoint allows for an easier calculation of localized deposition
  When electronic equilibrium exists with a photon source the charge deposition is highly localized near material interfaces
Notes: Adjoint Weight:
Electron Absorption + weight
Electron Production - weight

## Slide 3: Adjoint Particle Source for Charge Deposition
Extend MITS to charge deposition
  Combination of ITS and CEPXS
Developing a proper adjoint particle source
Modifications to the cross section form
  low-energy groups

## Slide 4: Adjoint Electron-Photon with ITS
Coupled electron-photon transport to solve Boltzmann-Fokker-Planck (BFP) equation
The adjoint BFP:
The 1st line contains the Boltzmann terms
The 2nd line contains the Fokker-Planck terms
  Represent electron interactions with small deflections or energy loss
α is the restrictive momentum transfer & S is the restrictive stopping power
Notes: Fokker-Planck Terms

## Slide 5: MITS
The Multigroup/Continuous-Energy (hybrid) Integrated TIGER Series (ITS)
CEPXS/ONELD cross-section generator
ITS input/output and combinational geometry routines
Converts the multigroup-Legendre format cross sections into cumulative probability distributions for CM scattering
A particle’s group index is needed for Boltzmann scattering
A particle’s discrete energy is needed for Fokker-Planck energy loss
Notes: Fokker-Planck Terms

## Slide 6: Boltzmann-Interaction Contributions to Charge Deposition
Requires accurate modeling of the lowest-energy electron group
  Most positive contributions to the electron deposition, will pass through the lowest-energy group
Finite total cross-section required for adjoint
  Cannot invert a non-finite cross section
  Used in calculating higher energy adjoint particles
Notes: Boltzmann inelastic cross section required for inversion
The scattering of the pseudo group is considered absorption

## Slide 7: Lowest-Energy Cross-Section
Introduce a Boltzmann interaction for the lowest group
  A pseudo-group is created for the lowest-energy group to “scatter” into
The Boltzmann-scattering cross section between adjoining groups
  Based on the transfer of particles between adjoining groups
  For the lowest group

## Slide 8: Adjoint Particle Weight
Adjoint particle weight at cutoff is equal to the stopping power
When adjoint particle speeds up between groups, its weight is adjusted by the ration of stopping powers
  Can use to determine the size of the pseudo-group
Adjoint particle weight in the lowest group can be defined as
Requires pseudo-group to have the same energy width as the lowest group
Notes: Therefore the pseudo group will have a small effective absorption cross section, flux will be constant in the group, multigroup approximation holds

## Slide 9: Modeling Geometries in ITS
ITS
Uses simple geometric shapes (sphere, cylinder, etc)
Combines geometries using Boolean operations
Efficient for computational run-time
  Combinational geometry makes intersection calculations for ray tracing easy
  All spaces is defined, even void
Enormous setup effort for complex geometries
  Some objects just cannot be accurately modeled

## Slide 10: Modeling Geometries
CAD
More accurate geometric representation
Faster setup time
  Some models may be preexisting in CAD format
Low geometric tolerances may result in history rejection
  Code can no longer follow particle trajectory if it slips into the cracks
Slower computationally
  Additional face intersection calculations required for ray tracing
  Not all space is well defined

## Slide 11: Developing CAD routine for ITS
ACIS file format was used
  Format will be automatically updated, no maintenance required
  Common format for several commercial CAD packages
Routines can interrogate the geometry in the following manner:
  Given a point and a direction, determine the closest boundary intersection.
  Given a point, identify the region enclosing that point
  Given a point on a surface, determine the outgoing surface normal
  Given a point, determine the minimum distance to a boundary

## Slide 12: Speeding up the CAD routine
A regular grid is superposed on the entire geometry
  A list is created of all regions that intersect each cell
  Entering a void only requires not being in all other regions within a cell
Create bounding volume around each part and each face
  If the ray misses the bounding volume, it misses the object within
Screens rays intersecting bounding volumes
  Object interrogated only if distance is closer than the closest object found
Code remembers which regions can be entered while exiting a given region
Code prevents the remaining zones from being checked more than once when determining where it is headed

## Slide 13
Questions?